## Slide 1: 1st National Conference on Sustainable Civil Engineering & Geospatial Technologies: Materials & Innovations for Climate Resilience (NCRT-SCE 2026) Buddha Institute of Technology GIDA, Gorakhpur Date of Conference: 15th – 16th April 2026
“ Comprehensive Analysis of Water Quality of Rapti River in Gorakhpur Region”
Under the Guidance
Mr. Rajan Shukla
Assistant Professor
Presented By:
Ajeet Yadav
2305250009004
4th Year
Department of Civil Engineering, BIT Gorakhpur

## Slide 2: Contents
Introduction
Problem Statement
Objectives
Literature Survey
Proposed Solution / Methodology
Results & Analysis
Conclusion & Future Work
Acknowledgements
References

## Slide 3: Introduction
Background:
In Gorakhpur, the Rapti River plays a dominant role in shaping the city’s geography, hydrology, and ecology.
The region lies in the middle Gangetic alluvial plains, which are fertile but highly flood-prone due to the river’s behavior.
Importance:
Supports aquatic ecosystems and biodiversity
Provides irrigation for large agricultural areas
Ensures safety and stability of excavation projects.
Context:
Water Quality Concerns.
Flood and Erosion Issues.
Urbanization and Population Pressure

## Slide 4: Problem Statement
Define the Problem:
Water Pollution.
Frequent Flooding.
Riverbank Erosion and Siltation.
Why it matters:
Environmental Impact.
Public Health Concerns.
Agricultural Dependency
Current Gap:
Lack of Integrated Studies.
Limited Pollution Source Identification.
Inadequate Use of Modern Techniques.

## Slide 5: Objectives
Objective 1: To access variation in water quality characteristics across different location in Gorakhpur .
Objective 2: Evaluate the presence and concentration of pollutants .
Objective 3: Identify the sources of pollution (domestic, industrial, agricultural runoff, etc.).

## Slide 6: Literature Survey
Yadav, D. & Pandey, G. (2021)- Gorakhpur is situated from bank of Rapti River. Rapti River is joined at Sohgaura with Ami River which is highly polluted as compare to Rapti River. Rapti River has a confluence into Ghaghra River at Kaparwar Ghat. The present study is conducted to determine the water quality of Rapti River using physical and Chemical parameters including pH, Turbidity, Total dissolved solids, Dissolved Oxygen (DO), and Total Hardness by collecting Three sets of samples from five locations from December, 2020 to February, 2021.
Mishra, KD (2020)- This paper illustrates the quality of Yamuna River water from the Agra region of Uttar Pradesh. This river is the second largest tributary of Ganga which flows from Uttrakhand to Haryana and then enters into Noida, Uttar Pradesh, and lastly merges into Ganga River at Triveni Sangam in Prayagraj, Uttar Pradesh.
Gond, M. & Pandey, G. (2017)- In this study, water quality evaluation was completed in 8 stations of Gorakhpur city. The study's point was to survey the physico-chemical parameters of drinking water quality from groundwater sources. It is found that the increment in the level of a portion of the physico chemical parameters of ground water has risen as a vital issue in urban areas.

## Slide 7: Proposed Solution / Methodology
RAJGHAT BRIDGE
BARHUAN
MOKSH DHAM
MUHAMDPUR MAPHI
TURBIDITY
ACIDITY
ALKALINITY
HARDNESS
pH VALUE
SAMPLING STATIONS
PARAMETERS
TDS
WATER SAMPLE
LABORATORY EXPERIMENTS
RESULT
CONCLUSION

## Slide 8: Results & Analysis
Chart: pH Value
| Rajghat | Barhuan | Mokshdham | Muhamadpur Maphi
August | 7.65 | 7.52 | 7.39 | 7.77
September | 7.67 | 7.91 | 7.86 | 7.91
Chart: Hardness(ppm)
| Rajghat | Barhuan | Mokshdham | Muhamadpur Maphi
August | 225 | 200 | 450 | 250
September | 280.25 | 260.23 | 300.27 | 240.21
Chart: Total Dissolved Solids Value
| Rajghat | Barhuan | Mokshdham | Muhamadpur Maphi
August | 121 | 140 | 167 | 140
September | 151 | 147 | 150 | 150
Chart: Turbidity (NTU)
| Rajghat | Barhuan | Mokshdham | Muhamadpur Maphi
August | 51.45 | 35.6 | 50.8 | 42.2
September | 53.23 | 33.68 | 47.8 | 45.69

## Slide 9: Conclusion & Future Work
The assessment of water quality parameters in the Rapti River revealed significant variations in physical, chemical, and biological characteristics.
The pH, hardness, alkalinity, and chloride content were found to be within the acceptable limits for drinking water, as per the Bureau of Indian Standards.
The assessment of water quality parameters of the Rapti River provides essential insights into the current status of river health and the potential impacts of natural and human-induced activities on this important freshwater resource.
In conclusion, this study emphasizes the importance of regular water quality monitoring, the need for sustainable water resource management, and the urgent requirement for pollution mitigation to ensure that the Rapti River remains a viable and safe water source for future generation.

## Slide 10: Acknowledgements
Guide:
I would like to express my sincere and heartfelt gratitude to my respected guide Mr. Rajan Shukla, Assistant Professor , Department of Civil Engineering, for his constant guidance, valuable suggestions, motivation, and continuous support throughout the completion of this research work. His technical expertise and encouragement helped me in successfully completing this study.
Institution:
I would also like to express my sincere thanks to Buddha Institute of Technology, Gorakhpur for providing a supportive academic environment, necessary resources, and infrastructure facilities which made this research work possible. I am also thankful to the Department of Civil Engineering for their cooperation and support.

## Slide 11: References
Sahni and Varshney; J. Appl. Chem. Sci. Int., vol. 15, no. 2, pp. 1-15, 2024; Article no. JACSI.12328.
Md. J. B. Alam, et al. Int. J. Environ. Sci. Tech., 4 (1): 159-167, 2007 ISSN: 1735- 1472.
Km Divya Yadav, Prof. Govind Pandey (Professor)Department of Civil Engineering.
Madan Mohan Malaviya University of Technology Gorakhpur U.P. India 273010 .
Ayush Kumar Rai; E. Moyo et al. Int. Journal of Engineering Research and Applications.
ISSN: 2248-9622, Vol. 5, Issue 7, (Part - 4) July 2015, pp.57-61
IOSR Journal of Biotechnology and Biochemistry (IOSR-JBB) ISSN: 2455-264X, Volume Issue 4 (Jul. – Aug. 2017), PP 08-15 www.iosrjournals.org
M. N. Uddin, M. S. Alam, M. N. Mobin and M. A. Miah; J. Environ. Sci. & Natural Resources,7(1): 253 – 260, 2014 ISSN 1999-7361
Pramod Kumar Vishwakarma; International Journal of Engineering Research & Technology (IJERT) ISSN: 2278-0181 Vol. 2 Issue 12, December – 2013

## Slide 12
Thank You